## Slide 1: Optical Pumping
Trapping Electrons With Light
Elijah K. Dunn
PHSX 516, Dec. 6, 2011

## Slide 2: Motivation
Demonstrate Zeeman Splitting
Determine the g-factor of Rb85 and Rb87
Optical pumping lab rarely gets completed by students
“It is only a small exaggeration to claim these [optical pumping] experiments constitute an atomic physics course.”
-TeachSpin Manual

## Slide 3: Zeeman Splitting
Fine and Hyperfine states from electron spin dipoles and orbit fields
In the presence of a magnetic field Hyperfine energy states () are split

## Slide 4: Induced Transitions
Electron in state
798.4 nm photon induces transition
Spontaneous emission
Emission in all directions
Start again!

## Slide 5: Pumping
Electrons emit a photon and loose energy
Electrons can deexcite to any Zeeman state with equal probability
Highest Zeeman state of the non-excited energy level can not gain a unit of angular momentum
Electrons cannot transition and will accumulate in that level
They have been “pumped” with optical waves!

## Slide 6: Zero Field Transition
Electrons are in the pumped state
Maximum transmission of light
Magnetic field diminishes to zero
Zeeman states collapse
Light transmission decreases as absorption increases

## Slide 7: EM Transition
Electrons are in the pumped state
Maximum transmission of light
Input EM wave matches the energy difference between Zeeman states
Transitions occur that drop the electrons out of the pumped state
Light transmission decreases as absorption increases

## Slide 8: Apparatus
RF discharge lamp
Optics
Pumping Cell
Optics
Detector
Magnetic Coils

## Slide 9: Optics
RF discharge lamp provides light
  Composed of Rb85, Rb87 and Xenon gas (buffer)
Plano-convex lens to collimate
Interference filter to transmit 798.4 nm light
Linear polarizer
¼ wave plate to circularly polarize light
  Ensures direction independent absorption
Plano-convex lens for focusing
Photodiode detector

## Slide 10: Magnetic Coils
Three pairs of Helmholtz coils
  Vertical field
    1.5 gauss/amp; 1.4 gauss max
  Horizontal field
    8.8 gauss/amp; 8 gauss max
  Horizontal sweep
    0.60 gauss/amp; 1 gauss max
Radio Frequency (RF) coil
  10 kHz – 100 MHz range
Homogeneity > 2 Gauss over cell

## Slide 11: Detection
Photodiode converts light to voltage
Oscilloscope plots photodiode voltage versus coil current
A decrease in light intensity: dip in the scope trace
Dip less than 1% magnitude
High gain (1-1000) allows easy detection
Zero Field Transition
Rb87 EM Dip
Rb85 EM Dip

## Slide 12: Methodology
Temperature stabilization
Alignment
Gain settings
Sweep the horizontal field
Locate Zero Field Transition
Minimize width with vertical field coil
Input EM wave
Search for EM dip
Change frequency

## Slide 13: Error and Uncertainty
Coil Current
  Current conversion less than 1% offset
  Voltmeter uncertainty (0.15%±2)
Inhomogeneity of Helmholtz coil fields
Alignment parallel to geomagnetic field
Area magnetic fields
  Moving elevator
  Metallic structure

## Slide 14: Results
mG

## Slide 15: Conclusions
Expected
is low
Demonstrated optical pumping for two isotopes
Magnetically isolate apparatus and measure R in the future

## Slide 16: Acknowledgements
My partner: S. Halder
Physics Dept. for providing the $14,000 Optical Pumping Apparatus
Prof. Han for suggestions and help